| Component parts to be tested in acc. to AITM 2.0007 | Dm 18 (flaming) | Dm 18 (non-flaming) |
| --- | --- | --- |
| Major Interior Panels • Ceiling and side wall panels • Dado panels • Door and door frame linings • Partitions • Overhead passenger service units • Cabin walls, e.g.: outer surfaces of lavatories, stowage compartments (other than underseat stowage compartments and compartments stowing small items), galley | 150 | Not required |
| Component parts to be tested in acc. to AITM 2.0007 | Dm 20 (flaming) | Dm 20 (non-flaming |
| • | Interior of compartments: e.g. Galley, lavatories, stowages | 200 | Not required |
| • | Major panels (covered by other than decor-laminate or paint) | 200 |  |
| • | Cargo liners | 100 |  |
| • • | Cabin floor panels19 Cargo floor panels | 200 |  |
| • | Seat cushion -& mattress | 200 | 200 |
| Floor covering • Carpets | 250 | 150 |
| • | Non-textile floor covering | 200 | 200 |
| • | Other components Airducting (without insulation) |  |  |
| • | Thermal and acoustic insulation blankets/ | 100 | 100 |
|  | components |  |  |
| • | Insulation Coverings |  |  |
| • | Airducting | (with insulation) | 200 | 150 |
| • | Transparencies, and thermoplastic parts | 200 | Not required |
| • | Equipment parts (incl. parts of seats, except |  |  |
| • | wire/cable) Elastomeric parts (used within the passenger | 200 | 200 |
|  | cabin and for air ducting) |  |  |
| • | Cable/wire | See paragraph chart below |
| Nonmetallic structural parts | 200 | Not required |

|  | Test method | Test time | Dm(flaming and non flaming) |
| --- | --- | --- | --- |
| Electrical wire and cable with the exception of electrical wire and cable for data transmission and RF-transmission lines installed as a single line or in harnesses | AITM 2.0008A | 16 min | 20 |
| Non electrical cable used for optical signal transmission installed in harnesses including power supply | AITM 2.0008A | 16 min | 20 |
| Non electrical cable used for optical signal transmission installed as a single line or in harnesses without power supply | AITM 2.0008B | 4 min | 200 |
| Electrical wire and cable used for data transmission and RF transmission lines installed in harnesses with a power supply >15 A | AITM 2.0008A | 16 min | 20 |
| Electrical wire and cable used for data transmission and RF transmission lines installed as a single line or in harnesses with a power supply ≤15 A | AITM 2.0008B | 4 min | 200 |
| Table 2: Smoke Density Limits for Electrical and Non Electrical Wire/Cable |